## Slide 1
CYBERSECURITY-AWARE COMMUNICATION FRAMEWORK
for OCC – Autonomous Vehicle Integration
using MQTT · OPC UA · DDS Security · VDA 5050
Moulikha Mahendran

## Slide 2
Research Gap & Motivation
Why this framework is needed in Industry 4.0
IDENTIFIED RESEARCH GAPS
01
Industrial protocols (MQTT, OPC UA, DDS) are evaluated in isolation — no unified OCC cybersecurity middleware framework exists.
02
Limited research integrates multi-protocol cybersecurity evaluation for autonomous industrial vehicle ecosystems.
03
No studies combine real-time KPI-based threat analysis with OCC communication middleware for AMR/AGV fleets.
04
VDA 5050 cybersecurity implications in autonomous fleet management remain unexplored in literature.
OUR CONTRIBUTION
Unified middleware framework bridging AMR/AGV to OCC
Multi-protocol comparative analysis under cyber threats
Real-time KPI evaluation with attack impact metrics
Attack simulation across 8 realistic cyber scenarios
3
Raspberry Pi Nodes
4
Protocols
8
Attack Scenarios
10+
KPI Metrics

## Slide 3
Layered System Architecture
4-layer cybersecurity-aware OCC integration framework
LAYER 1 · AUTONOMOUS VEHICLE LAYER
3× Raspberry Pi | Synthetic Telemetry | AGV/AMR Simulation | KPI Generation
LAYER 2 · COMMUNICATION PROTOCOL LAYER
MQTT/TLS · OPC UA · DDS Security · VDA 5050
LAYER 3 · CYBERSECURITY MIDDLEWARE (CORE)
Threat Detection · Protocol Handler · KPI Engine · Traffic Monitor · Security Decision
LAYER 4 · OCC DASHBOARD LAYER
Vehicle Monitor · Attack Alerts · Protocol KPI Graphs · Anomaly Warnings

## Slide 4
Cybersecurity Middleware Framework
Internal module architecture the core research contribution
INPUT & ROUTING
Data Receiver
Multi-vehicle, multi-protocol ingestion
Protocol Handler
MQTT / OPC UA / DDS / VDA 5050 parsing
Data Validation
Schema, range & integrity checks
SECURITY CORE
Threat Detection Engine
ML + rule-based anomaly detection
Traffic Monitoring
Real-time packet & flow analysis
Attack Analysis
Attack fingerprinting & classification
OUTPUT & CONTROL
Security Decision Layer
Block / alert / quarantine logic
KPI Measurement
Latency, throughput, jitter, loss
Data Forwarding
Verified telemetry → OCC dashboard
Middleware processes all incoming vehicle data before OCC visibility · No unvalidated traffic reaches the dashboard · Attack classification runs in < 50ms

## Slide 5
Multi-Protocol Comparative Analysis
MQTT · OPC UA · DDS Security · VDA 5050 evaluated under cybersecurity lens
Metric
MQTT / TLS
OPC UA
DDS Security
VDA 5050
Real-Time Capability
★★★★☆
★★★★☆
★★★★★
★★★☆☆
Cybersecurity Strength
★★★☆☆
★★★★★
★★★★★
★★★☆☆
OCC Compatibility
★★★★★
★★★★☆
★★★☆☆
★★★★★
Scalability
★★★★★
★★★☆☆
★★★★★
★★★★☆
Industrial Suitability
★★★★☆
★★★★★
★★★★☆
★★★★★
Protocol Overhead
Low
Medium
Medium
Low
Encryption Native
TLS (ext.)
Native
Native
Optional
Authentication
Token/TLS
X.509 PKI
DDS Auth
Role-based
KEY INSIGHT: DDS Security provides the strongest real-time + security combination. OPC UA excels in PKI integration. MQTT suits lightweight fleet communication. VDA 5050 is the AGV industry standard.

## Slide 6
Protocol-Specific Data Flow Architecture
End-to-end communication pathways for each protocol
MQTT/TLS
Vehicle Node
MQTT Broker (Mosquitto)
Middleware Client
OCC Dashboard
OPC UA
OPC UA Server (Pi)
Middleware UA Client
Security Filter
OCC Dashboard
DDS Security
DDS Publisher (Pi)
DDS Subscriber
RT Middleware
OCC Dashboard
VDA 5050
AGV Fleet Node
VDA 5050 Broker
Middleware Engine
OCC Dashboard
MIDDLEWARE

## Slide 7
Cyber Attack Simulation Scenarios
8 threat scenarios evaluated against the middleware framework
AS-01
High
DoS / Flooding
DETECTION:
Rate Limiter + Threshold
KPI IMPACT:
Latency ↑↑ Throughput ↓↓
AS-02
Critical
MITM Attack
DETECTION:
TLS Certificate Validation
KPI IMPACT:
Integrity ↓↓ Trust ↓↓
AS-03
High
Fake Vehicle
DETECTION:
Auth Token + Fingerprint
KPI IMPACT:
False Data Injection
AS-04
Medium
Packet Replay
DETECTION:
Timestamp + Sequence Check
KPI IMPACT:
Jitter ↑ Duplicates ↑
AS-05
Critical
Packet Tamper
DETECTION:
Hash Validation / HMAC
KPI IMPACT:
Data Integrity ↓↓
AS-06
High
Network Pivot
DETECTION:
Lateral Traffic Monitor
KPI IMPACT:
Network Overhead ↑↑
AS-07
Low
Anomaly Traffic
DETECTION:
ML Anomaly Classifier
KPI IMPACT:
Baseline Deviation
AS-08
None
Normal Baseline
DETECTION:
N/A – reference only
KPI IMPACT:
All KPIs nominal
All attack scenarios are reproducible on Raspberry Pi testbed · Middleware logs detection timestamps and KPI deltas for each scenario

## Slide 8
KPI Evaluation Framework
10 performance & security metrics across all protocols and scenarios
KPI Metric
MQTT/TLS
OPC UA
DDS Sec.
VDA 5050
Latency (ms)
12–40
25–80
5–20
15–50
Throughput (msg/s)
1000+
200–500
5000+
300–800
Packet Loss (%)
0.1–2
0.05–1
< 0.1
0.2–3
Jitter (ms)
2–15
5–20
1–5
5–25
Security Overhead
Low
High
Medium
Low
Recovery Time (ms)
50–200
100–500
20–100
80–300
Detection Accuracy
88%
95%
97%
85%
CPU Usage (%)
15–30
40–70
20–45
18–35
■ GOOD
■ MODERATE
■ POOR
(Values shown: normal operation baseline)

## Slide 9
7-Phase Implementation Roadmap
Structured research-to-deployment execution plan
PH 1
Environment Setup
• Python 3.10+
• Raspberry Pi OS
• Mosquitto MQTT
• OPC UA libs
• DDS tools
PH 2
Vehicle Simulation
• AGV telemetry gen
• Speed / Position
• Battery modeling
• Task scheduler
• Timestamp sync
PH 3
Protocol Impl.
• MQTT pub/sub
• OPC UA server
• DDS topics
• VDA 5050 msgs
• TLS certs
PH 4
Middleware Core
• Threat detection
• KPI measurement
• Traffic monitor
• Security layer
• Data forwarding
PH 5
Attack Simul.
• DoS flooding
• MITM scripts
• Fake vehicle
• Replay attack
• Packet tamper
PH 6
Dashboard UI
• React frontend
• Live KPI charts
• Attack alerts
• Anomaly view
• Protocol graphs
PH 7
KPI Analysis
• Stats analysis
• Report gen

## Slide 10
OCC Dashboard Architecture
Real-time operational control center visualization concept
OCC CYBERSECURITY DASHBOARD ◉ LIVE | Vehicles: 3 | Threats: 0 | Protocol: MQTT / OPC UA / DDS / VDA 5050
AGV-001 ● ONLINE
Speed: 38 km/h
Batt: 85%
Pos: X12 Y8
Task: ACTIVE
AGV-002 ● ONLINE
Speed: 42 km/h
Batt: 75%
Pos: X13 Y9
Task: ACTIVE
AGV-003 ● ONLINE
Speed: 46 km/h
Batt: 65%
Pos: X14 Y10
Task: ACTIVE
Chart: Protocol Latency (ms)
| T1 | T2 | T3 | T4 | T5 | T6
MQTT | 12 | 15 | 14 | 18 | 13 | 16
OPC UA | 28 | 32 | 30 | 35 | 29 | 31
DDS | 8 | 9 | 7 | 10 | 8 | 9
Chart: Throughput Comparison
| MQTT | OPC UA | DDS | VDA 5050
Throughput (msg/s) | 980 | 420 | 4800 | 650
■ SECURITY EVENT LOG
All clear — No active threats detected ● Last scan: 0.3ms ago ● Packets analyzed: 14,832 ● Anomalies: 0
Middleware status: ACTIVE ● Detection engine: RUNNING ● KPI engine: RUNNING ● All protocols: HEALTHY

## Slide 11
Autonomous Vehicle Layer — Testbed Design
3× Raspberry Pi nodes simulating AGV/AMR behavior
AGV-001 (Pi #1)
Speed:
30 km/h
Position:
X10 Y5
Battery:
90%
Task:
ACTIVE
Net ID:
N001
Protocol:
MQTT
AGV-002 (Pi #2)
Speed:
38 km/h
Position:
X11 Y6
Battery:
82%
Task:
ACTIVE
Net ID:
N002
Protocol:
OPC UA
AGV-003 (Pi #3)
Speed:
46 km/h
Position:
X12 Y7
Battery:
74%
Task:
ACTIVE
Net ID:
N003
Protocol:
DDS
VEHICLE KPI BROADCAST
speed
position
battery
task_status
timestamp
network_id
packet_seq
checksum

## Slide 12
Research Contributions & Future Directions
Summary of academic and industrial value
KEY RESEARCH CONTRIBUTIONS
Novel unified cybersecurity middleware framework for OCC–AMR/AGV communication
First comparative security evaluation of MQTT, OPC UA, DDS, and VDA 5050 in an OCC context
KPI-based threat detection linking communication metrics to security decisions
8-scenario attack simulation testbed on resource-constrained Raspberry Pi hardware
Real-time security dashboard with anomaly visualization for operational control centers
PUBLICATION POTENTIAL
· IEEE Industrial Informatics · IEEE Transactions on Ind. Cyber-Physical Systems · ETFA / ISORC Conference
FUTURE DIRECTIONS
→ ML-based zero-day detection
→ 5G & TSN integration
→ Hardware security modules (HSM)
→ Digital twin cyber simulation
KEYWORDS:
Cybersecurity Middleware · OCC Integration · MQTT · OPC UA · DDS Security · VDA 5050 · AMR/AGV · Industry 4.0 · Cyber-Physical Systems · KPI Analysis · Threat Detection · Raspberry Pi Testbed